## Slide 1
Smart Metering Development
Tczew, XI 2012 r.

## Slide 2
Continued cooperation with Flonidan A/S in development of GxS line meters
UniSmart: Telemetry Module
Automatic Meter Reading
  Walk-by and Drive-by systems
  Stationary systems
Smart Components Development
  Shut-Off ball Valve with stepper motor
  New Cable Transfer
  Modular design of New Metrix EU
New Fields for Cooperation
  Secure Meters Ltd.
  GWi
Metrix employee are members of:
  OMS workgroup
  prEN16314 Additional Functionalities WG
Smart Metering Development

## Slide 3
New Smart Meters GxS series combine all the best features and capabilities of previous models :
Reliable, resistant to interference, optical pulse readings from measuring unit, using a Gray code wheel
Much better metrological accuracy due to error curve correction
Temperature compensation
Internal shutt-off valve
Volume and Alarms registarion
Remote safe reading using AES-128 encryption
Wired/Wireless communication EN-13757
GxS Smart Gas Meters
NTA8130 + DSMR v.2.2/2.3/3.0

## Slide 4
Compact design
MID Class 1,5
ATEX II 1/2 G Ex ia/ib IIB T3
IP-54
Over 15 battery life time
Notes: Komunikacja przewodowa lub bezprzewodowa (M-BUS) wg EN13757-4
IP54: Ochrona przed wnikaniem pyłu w ilościach nie zakłócających pracy urządzenia;
Ochrona przed kroplami padającymi pod dowolnym kątem, ze wszystkich stron (deszcz)
ATEX II 1/2 G Ex ia/ib IIB T3
G – Rodzaj zagrożenia: gazy, ciecze i ich opary
1/2 1 Sporadyczne, zagrożenie może się pojawić w normalnych warunkach
2 Rzadkie, nie występuje w warunkach normalnej pracy, jeżeli wystąpi, to przez krótki okres
Ex ia/ib: Rodzaj ochrony przeciwwybuchowej: iskrobezpieczny
IIB Urządzenia przeznaczone do pracy na powierzchni w obszarach zagrożonych wybuchem gazów, par, mgieł lub pyłów; Grupa etylenowa (np. etylen, siarkowodór)
T3 maksymalna temperatura powierzchni 200 stopni Celsjusza; temperatura zapłonu gazu 200÷300 Celsjusza

## Slide 5
Electronic Unit has the ability to compensate for the effect of temperature on the measurement error.
Temperature correction is performed in a volume of 4 points: -25, 0, +30, +55 C. Between these points, linear interpolation is used
Temperature compensation
Chart: temperature
| -16 | -13 | -10 | -7 | -4 | -1 | 2 | 5 | 8 | 11 | 14 | 17 | 20 | 23 | 26 | 29 | 32 | 35 | 38 | 41
błąd | 0.11999 | 0.10999 | 0.09999 | 0.089991 | 0.079992 | 0.069993 | 0.059994 | 0.049995 | 0.039996 | 0.029997 | 0.019998 | 0.009999 | 0 | -0.01 | -0.02 | -0.03 | -0.04 | -0.05 | -0.06 | -0.07
Temperature sensors

## Slide 7
Curve error correction
Much better measurment accuracy
errors below limit ± 0,3% !!!

## Slide 8
From magnetic coupling…
… to optical Gray code reading
Evolution instead of Revolution
Notes: Ruch jednostki pomiarowej wykrywany przez układ detekcji optycznej bazujący na kole kodowym Gray’a

## Slide 9
Realiable pulse reading method use 3 optical sensors, allowing to measure with ressolution of 1/8 rotation of measuring unit cyclic volume.
Optical pulse reading is tamper proof against magnetic fields
Gray code wheel…
phototransistors
Notes: Czujniki optyczne nie mogą być zakłócone przez magnesy neodymowe jak rozwiązania na kontraktronie. Czujniki optyczne wykrywają próbę ingerejci

## Slide 10
1 | 2 | 3
1 2 3
Gray code wheel …
Notes: Styk normalnie otwarty, 3 bitowy przetwornik, więc 2*2*2=8 impulsów na obrót daje rozdzielczość pomiarową 1/8 obrotu. 1 Obrót = 1 objętość cykliczna baterii gazomierza czyli w naszym przypadku 1,2l lub 2,2l a wkrótce również 2,4l.
Dla baterii 1,2l => 1 impuls = 0,15 l
Dla baterii 2,2l => 1 impuls = 0,275 l
Dla baterii 2,4l => 1 impuls = 0,3 l

## Slide 11
1 | 2 | 3
1 2 3
Gray code wheel …

## Slide 12
1 | 2 | 3
1 2 3
Gray code wheel …

## Slide 13
1 | 2 | 3
1 2 3
Gray code wheel …

## Slide 14
1 | 2 | 3
1 2 3
Gray code wheel …

## Slide 15
1 | 2 | 3
1 2 3
Gray code wheel …

## Slide 16
1 | 2 | 3
1 2 3
Gray code wheel …

## Slide 17
1 | 2 | 3
1 2 3
Gray code wheel …

## Slide 18
New Cable Transfer
The seals are capable of remaining hermetic after exposure to 820°C
The leakage rate of the seal after exposure to 820°C would be better than 1x10-6 cc per sec of helium.

## Slide 19
GSU shutt-off valve
Safe, internal, build-in new generation of ball valve:
  Safe open function
  Low pressure drop in comparison to competitive designs
  Two state valve position control (fully closed / fully open), confirmed by realiable microswitch designed to work in gas and oil enviroment
  Installation on the gas meter outlet (less contamination)
  Higher Intrinsically Safty - using industriy field proven stepper motor manufactured by Johnson Electric Group ®
Notes: Bezpieczny, wbudowany zawór nowej generacji:
  Funkcja bezpiecznego otwierania – na wylocie gazomierza
  Niskie straty ciśnienia w porównaniu do funkcjonujących rozwiązań
  Dwustanowa kontrola stanu zaworu – wykrywa stan wpełni otwarty, wpełni zamknięty
  Funkcje autodiagnostyki
  Montaż na wylocie gazu z gazomierza
  Liniiowy silnik prady stalego zawiera szczotki, które nie używane w cyklu życia mogą się utleniać, rośnie ich rezystancja w finale przestają przwodzić prądu i silnik nie działa.
  Silnik krokowy ma bezstykowe

## Slide 20
Pressure drop
up to
(Qmax@G10)

## Slide 21
Two state position control
Microswitch

## Slide 22
Modular design:
UG-NL 220 mm adapter

## Slide 23
Modular design:
UG-EN 6” (152,4 mm)

## Slide 24
Modular design:
UG-F 130 mm

## Slide 25
Flexibility
Comaptible with all UG meters
1,2 dm3
2,2 dm3

## Slide 26
Design challenges
Design optimalization using CFD
Computional Fluid Dynamics

## Slide 27
Pressure drop acc. CFD ~0,2 mbar
CFD simulations
Real pressure drop ~0,15 mbar
Other models
<0,05 mbar

## Slide 28
CFD optimized adapter of:
UG-F 110 mm

## Slide 29
UG-NL 220 mm

## Slide 30
UG-NL 220 mm

## Slide 31
UG-NL 220 mm

## Slide 32
UG-NL 220 mm

## Slide 33
UG-F 130 mm

## Slide 34
UG-F 130 mm

## Slide 35
UG-F 130 mm

## Slide 36
UG-F 130 mm

## Slide 37
UniSmart: telemetry module
Communication
Pulse counting
  1 pulse = 1 full rotation of last counter roller (for meters G1,6 - G6 1 puls=10dm3, for meters G10 1 ipuls=100dm3)
  Algorithm of errors elimination such as errors due to mechanical vibration of rollers in counter.

## Slide 38
The conversion of the volume pulse(m3);
Flows history (60-dayly, 120-monthly);
Alarm registers:
  Interference by an external magnetic field;
  Exceeding the maximum flow(Qmax);
  Lack of pulse.
Bootloader (possibility of remote firmware upgrade) under development Datagram Encryption AES-128 acc EN13757-3:
  OMS (with dynamic initialization vector);
  NTA (with dynamic initialization vector); possible development
  NTA (with static initialization vector). possible development
Power supply: 1x lithium battery type AA;
Battery Operation 10 years
UniSmart: Functionality

## Slide 39
AMR (ang. automatic meter reading)
Remote reading system
  Walk-by system
Stationary system

## Slide 40
Walk-by system

## Slide 41
Inkasent PDA application

## Slide 42
PSION Terminal
  Mobile terminal PSION WORKABOUT PRO

## Slide 43
Stationary system

## Slide 44
File generating *.csv
GSM hubs can supply with solar panels
Data Concentrator (MUC) under development

## Slide 45
GSM Hubs:
Power supply 230 V AC
Solar panels power supplies
Data Concentrator (MUC) under development

## Slide 46
M-BUS retransmitter
under development
Retransmitters
Power supply 230 V AC
Baterry supply

## Slide 47
Pilot Instalation in:
Wielkopolskiej Spółka Gazownictwa S.A.

## Slide 48
Pilot Instalation in WSG S.A.
GxS Smart Meters has been used in the pilot with OMS protocol communication.
Meters configuration includes:
  Error curve correction (Vc)
  Base Volume conversion (Vb)

## Slide 49
Additional Functionalities Implemented during pilot instalation
  Solution from Smart Gas Meter side which allows Customer to balancing the gas network system.
  Interopability: Overall system has been integreated to fit both for existing aplication systems and at device level too.
  We have been greatfull to receive interest from National Notified Body of Oil and Gas (INiG). Cooperation with INiG can enhance an ongoing Project

## Slide 50
More then 2000 GxS Smart Gas Meters
Drive-by reading by PSION WORKABOUT PRO 3 and car roof antenas

## Slide 51
Walk-by / Drive-by
  PSION WORKABOUT PRO

## Slide 52
Drive-by AMR reading

## Slide 53
External car roof antena 868 Mhz

## Slide 54
Terminal PSION WORKABOUT PRO 3

## Slide 55
Screenshoots from mobile app

## Slide 56
Screenshoots from mobile app

## Slide 57
Aplikacja Inkasent Mobile
Screenshoots from mobile app

## Slide 59
Customer Customization

## Slide 60
Prepayment ZigBee Smart Gas Meter Project

## Slide 62
Project database

## Slide 63
Thank you for your attention